## Slide 1
LocalSWMM — The OpenSWMM 6 Engine, in the Browser
A WebAssembly-powered web GUI for stormwater & wastewater modeling · Research & technical overview of the engine, the GUI, the 1D scheme, and the roadmap
LocalSWMM · https://swmm6.is-local.org · 2026

## Slide 2
01
The Opportunity

## Slide 3
The Gap: SWMM 6.0 is community-driven
– US EPA has not released SWMM 6.0 — the official page still lists SWMM 5.2.4 (2023)
– The 6.x line lives only in the community: the HydroCouple OpenSWMM engine (a fork of the EPA repo)
– OpenSWMM 6.0.0-alpha.1 debuted May 2026 (alpha.3 current)
– Rewritten in C++20: data-oriented (Structure-of-Arrays), reentrant engine, plugin I/O on a dedicated thread, Kokkos GPU backends
– New hydraulics: semi-implicit node continuity, Anderson acceleration, finite-volume routing, 1D/2D coupled overland flow
LocalSWMM · OpenSWMM 6
3

## Slide 4
A First-Mover Gap
– The official WebAssembly bindings repo (openswmm.engine.wasm) is an empty stub
– Few projects build on the v6 engine: a desktop Qt GUI, a batch runner, Python/agent tooling
– LocalSWMM is the only full, map-based browser GUI on OpenSWMM 6
– Created 2 days after alpha.1 (May 2026) — early position in a nascent ecosystem
LocalSWMM · OpenSWMM 6
4

## Slide 5
State of the Project
– 100% in-browser: editor, mesher, and engine run in the browser — no backend, no database
– ~15,000 lines of dependency-free JavaScript (classic IIFEs) + Mapbox GL JS
– Stable: 1D editor + engine pipeline. Experimental: 2D module + opt-in WebGPU marcher
– Engine pinned as a git submodule (HydroCouple fork + wasm-compat fixes)
– Deploys: Cloudflare Pages (production, threaded build) + GitHub Pages (no threads)
LocalSWMM · OpenSWMM 6
5

## Slide 6
02
The Engine in the Browser

## Slide 7
Architecture — Client-Side Only
– The OpenSWMM engine compiled to WebAssembly with Emscripten
– Data flow: model → INP → worker → WASM engine → .rpt/.out → results (tables, map, plots)
– The only server: static files + a health endpoint (GET /api/status)
– Two simulation backends: the WASM engine (1D + 1D/2D) and an experimental WebGPU solver
LocalSWMM · OpenSWMM 6
7

## Slide 8
C++ → WASM with Emscripten
– clang/LLVM compiles C++20 to a WebAssembly binary + JS glue loader
– vcpkg-managed deps: eigen3, hdf5, nlohmann-json, sundials — wasm32-emscripten triplet, static
– CMake wrapper flags: MODULARIZE, EXPORT_NAME createOpenSwmm2D, ALLOW_MEMORY_GROWTH, FILESYSTEM=1 (MEMFS)
– Result: ~4.8 MB .wasm + ~91 KB glue; async streaming compile, pre-warmed in a worker at page load
LocalSWMM · OpenSWMM 6
8

## Slide 9
The C API Bridge
– 31 exported symbols: swmm_engine_*, swmm_2d_*, swmm_node_*, malloc/free
– Engine runs inside a persistent Web Worker; a fresh instance per run (~10–50 ms)
– Model in: FS.writeFile('/in.inp') · results out: FS.readFile('/rpt.rpt' + '/out.out')
– A stride() loop drives the simulation; the binary .out is parsed zero-copy (Float32Array views)
LocalSWMM · OpenSWMM 6
9

## Slide 10
Threading & Cross-Origin Isolation
– OpenMP solver loops map to Emscripten pthreads → SharedArrayBuffer
– SharedArrayBuffer is gated behind COOP/COEP headers — the page must be cross-origin isolated
– Cloudflare Pages serves the headers (production); GitHub Pages cannot → no threaded build there
– PTHREAD_POOL_SIZE=4 pre-spawns workers; blocking waits run on a worker thread, never the UI
LocalSWMM · OpenSWMM 6
10

## Slide 11
A Browser Engine: Advantages vs Disadvantages
Advantages
– Privacy: models never leave the device — no server, no account
– Offline-capable, zero-install, cross-platform
– No server cost; scales to zero
– The same C++ codebase builds native AND wasm
– Sandboxed, near-native scalar speed
Disadvantages
– Threads gated by cross-origin isolation
– Partial SIMD (scalar build on Linux; -msimd128 on Windows)
– Browser memory ceilings (128 MiB initial, wasm32)
– Bespoke build: emsdk + vcpkg + patched engine
– Per-client horsepower, not per-cluster
LocalSWMM · OpenSWMM 6
11

## Slide 12
03
The GUI — What the User Builds

## Slide 13
The Network Editor
– Nodes: junction, outfall, storage, divider, rain gage · Links: conduit, pump, weir, orifice
– Subcatchments drawn as polygons; undo/redo, snap & drag, schema-driven properties panel
– Import: .json, SWMM .inp, shapefile (.zip), DXF, GeoJSON · Export: .inp / .json
– Coordinate systems: WGS84, UTM/EPSG, local; import as network or reference layers
LocalSWMM · OpenSWMM 6
13

## Slide 14
Simulation Options
– Flow routing: Kinematic / Dynamic Wave / Steady / Finite Volume (FV)
– Advanced FV panel: CFL, Riemann solver (HLLC/HLL), order, limiter, LTS, node coupling…
– Node continuity: Legacy / SEMI_IMPLICIT · Anderson acceleration · RDII recovery (k0, kT, Tref)
– 2D mesh dialog: terrain sources, mesh quality, hydraulics & solver defaults
LocalSWMM · OpenSWMM 6
14

## Slide 15
Run & Results
– Run Status: live progress in simulated time (real for the 2D path; engine version stamped)
– Time slider: play/pause/speed over steps; map coloring via Mapbox feature-state
– Results tables: node depths/inflows, link flows, subcatchment runoff + KPI cards, sparklines
– Hydraulic profile & time-series plots; 2D frames (depth/head/velocity) + WebGPU marcher
LocalSWMM · OpenSWMM 6
15

## Slide 16
Mapbox 3D
– 3D View: Mapbox terrain + extruded buildings
– 3D Net: network geometry extruded via fill-extrusion — manholes, pipes, weirs/orifices/pumps
– Geometry driven by the SWMM model (inverts, cross-sections) — not by Mapbox data
– Simulation result colors mirrored onto the 3D extrusions across the time slider
LocalSWMM · OpenSWMM 6
16

## Slide 17
04
The 1D Calculation Scheme

## Slide 18
The 1D Scheme Today (Dynamic Wave)
– Per step: time-step control → runoff → link momentum kernel → node depth update → Picard convergence (8 trials, head tol 0.005 ft)
– Momentum: implicit St. Venant, six per-barrel contributions; Froude-based partial-inertia damping
– Node continuity: trapezoidal volume change; default EXPLICIT + EXTRAN surcharge slot
– Opt-in SEMI_IMPLICIT unifies free-surface and surcharge in one smooth equation
LocalSWMM · OpenSWMM 6
18

## Slide 19
Engine Modifications LocalSWMM Adds
– Anderson acceleration: −25–50% Picard iterations on stiff transitions
– Dynamic Preissmann slot: transient-storage slot without 'slot squeezing'
– Virtual junctions: zero-storage chambers for slope breaks
– Finite-volume routing (FV): conservative Godunov solver, LTS up to 6 tiers, native transcritical & dry/wet
– RDII decay recovery; 1D↔2D coupling (orifice law, live exchange)
LocalSWMM · OpenSWMM 6
19

## Slide 20
1D Roadmap
– FV routing being wired end-to-end into the UI (dropdown + advanced options, parser/exporter)
– Semi-implicit + Anderson path hardened by recent engine fixes (continuity sign, double-count)
– Reality check: the 1D dynamic wave is ≈90% of wall time — speed knobs measured and rejected (fidelity)
– WebGPU marcher: M0–M3 done, M4/M5 pending; opt-in — 0.13 ms/substep 2D, not yet faster overall
LocalSWMM · OpenSWMM 6
20

## Slide 21
05
Deep Technical

## Slide 22
How Street View Rendering Works
– Google StreetViewPanorama embedded in the Mapbox editor (Pegman button)
– Network re-projected onto the pano plane: haversine range/bearing + gnomonic pinhole model
– Terrain correction: Mapbox queryTerrainElevation, fallback to Google Elevation API (batched, cached)
– Drawn on a pointer-events-none canvas; rAF-coalesced redraws; Mapbox camera synced to the pano
LocalSWMM · OpenSWMM 6
22

## Slide 23
Server-Side Migration — the Scaling Plan
– Today: the engine runs 100% in the browser (WASM); only GET /api/status exists
– Planned: a native service with a pool of workers (one process per core) + a queue
– EngineClient seam: Modo local (WASM) vs Modo API (default) — the same GUI, two engines
– API: submit a corrida, progress by ID (real sim-time), results (.out/.rpt/JSON + 2D frames), system state
– The same C API the browser uses; the native build drops the pthread/SAB constraints
LocalSWMM · OpenSWMM 6
23

## Slide 24
06
Future

## Slide 25
User Model Library on Free Cloud
– Google Drive: 15 GB free per user, API free today, browser-only OAuth with the drive.file scope (no verification, no 100-user cap)
– Alternatives: GitHub Gists (text-only, ≤1 MB), Dropbox (2 GB), Cloudflare R2 (10 GB, needs backend), Supabase (1 GB, pauses)
– Recommended: Drive for user libraries; R2/Supabase later for server-side results storage
LocalSWMM · OpenSWMM 6
25

## Slide 26
Roadmap Summary
– Keep the WASM path for privacy & offline; add the native pool for runs too heavy for one tab
– Finish FV routing UX and harden the 1D numerics; land WebGPU M4/M5
– Ship the user model library (Drive) and the EngineClient seam
– Position LocalSWMM as the reference web GUI for OpenSWMM 6
LocalSWMM · OpenSWMM 6
26